## Slide 1: IsoDAR 60 MeV/amu Simulations Sensitivty Studies
Daniel Winklehner PSI/MIT Meeting, Sep 14th, 2020

## Slide 2: Cyclotron/OPAL Overview – harmonic 4
OPAL:
  Track 1e5 particles
  Single bunch
  32^3 mesh – FFT solver (no boundaries)
  42° cavity opening angle, f = 32.77 MHz
  1000 steps per turn – 104 turns
  Start with Gaussian matched distribution  4 sigma truncation
  Probe at 30°
  Each cavity has 2 idealized 10 mm accelerating gaps with a radial profile V(r) from 70 kV-250kV
  Magnetic field given on median plane only  OPAL calculates z ≠ 0 components from series expansion.

## Slide 3: Initial beam parameters
Gaussian matched distribution at 193 keV/amu
Max. Height: ~3 cm, Length ~2.6 cm, Width ~0.8 cm
1-RMS, normalized emittance:
  vertical: 0.6 mm-mrad
  Radial: 0.14 mm-mrad

## Slide 4: Collimators
Initial particle angle: -135°
5 Collimators
1e5 particles total

## Slide 5: Probe 2 Data (30° from pos x-axis)
septum
23% Loss on collimators
132 W on septum

## Slide 6: Procedure to add electrostatic deflectors (ESD)
Run OPAL up to 98 turns, saving particle data 2-4 times per turn
Re-run OPAL from 98 to 104 turns with high resolution
Use h5 output file to generate ESD1  Inventor  COMSOL  OPAL
Re-run OPAL turn 98 to 104 with new fields and CCOLLIMATORs
Use new trajectory to generate ESD2
Do twice to make ESD’s follow new trajectory instead of original one

## Slide 7: CAD  Electrostatic Field
Python Script  Inventor Macro  Model
Iges import  COMSOL  Field  OPAL h5part format

## Slide 8: Preliminary Result
E

## Slide 9: Sensitivity Study
This is getting us close to start-to-end…so, here is the plan:
Devin is working on refinement and analysis of output beam
Daniel is working on tracking beam through spiral inflector
Sonalie will begin a sensitivity study, varying the input beam parameters:
  (Have begun already with current variation)
  Beam radial position
  Beam radial momentum component
  Bunch phase
  Beam size
rbunch
pr
pl

## Slide 10: Discussion: Data Exchange
Git repo for simulation decks and analysis python scripts: https://github.com/DanielWinklehner/isodar-60mev.git
Midplane magnetic field maps and voltage profile - OK
How to share the large 3D field maps and h5 output files?
  Dropbox (limited to 2 TB with Pro account)
  Fileserver
  Combos (maybe this: https://github.com/anishathalye/git-remote-dropbox)
Maintain good workflow (we need to establish this)
Maintain good documentation